## Slide 1
Energy Saving in O-RAN with Reinforcement Learning
A digital-twin study: learning to sleep 5G cells without hurting service quality
ns-3 mmWave O-RAN · imitation + PPO · energy-vs-QoS tradeoff

## Slide 2
The problem & the goal
• 5G base stations (gNBs) draw ~600 W even when almost idle — a large, avoidable energy cost.
• Idea: an intelligent controller that puts unused gNBs to sleep, waking them when demand returns.
• The tension: sleep too aggressively and you drop calls / lose throughput (QoS).
• Company goal: a reinforcement-learning (RL) controller that beats the hand-coded heuristic on the
  – energy-vs-QoS tradeoff — more energy saved without hurting throughput or reliability.

## Slide 3
The digital twin (what we simulate)
• ns-3 mmWave O-RAN simulator, scenario-three: 1 LTE anchor cell + 7 mmWave gNBs (can sleep), 6 users.
• Traffic redesigned to 3 sharp bursts per episode (+ an always-on baseline user) — so the controller
  – must adapt in real time (sleep in the lulls, wake for the bursts).
• Energy model: each ON gNB = 600 W static + 400 W x utilisation; a sleeping gNB ~ 0 W.
• Key constraint: the simulator runs ~15-20 s per 100 ms control step (CPU-bound) — this shapes everything.

## Slide 4
How it works — real-time closed-loop control
• Every 100 ms, a handshake over shared memory (files + semaphores):
  – ns-3 emits per-cell KPMs (load, throughput, dropped calls) -> a 61-number observation.
  – the controller picks a 7-bit ON/OFF action (one bit per gNB; anchor always ON).
  – the action is written back; ns-3 applies it and advances 100 ms.
• Reward the RL optimises: throughput(Mbps) - energy(kW) - 2 x dropped-calls(RLF).
• The controller plays the role of an O-RAN 'xApp'; we drive the sim directly (no live RIC needed).

## Slide 5
The controllers we compared
• Heuristic (TwinHeuristic) - the company baseline: load-adaptive, sleeps idle cells, wakes on neighbour load.
• Behaviour Cloning (BC) - a neural net trained to copy the heuristic (reached 100% match).
• PPO (reinforcement learning) - warm-started from BC, then fine-tuned on the reward. The one that can surpass.
• Pruning controller - an aggressive energy-saver with a tunable 'grace' dial (energy-vs-reliability).
• (ns-3's own built-in heuristic is quota-driven and can't adapt to load - hence the custom one.)

## Slide 6
The learning pipeline
• 1) Collect expert demonstrations - run the heuristic on the twin, log (observation, action) pairs.
• 2) Behaviour Cloning (+ critic warm-up) - clone the heuristic into the policy AND pre-train its value
  – estimator; the warm-up fixes a classic BC->PPO collapse we hit and diagnosed.
• 3) PPO fine-tune (~4 h, live ns-3 rollouts) - improve on the true reward.
• 4) Evaluate deterministically vs the heuristic across 4 seeds; score energy / throughput / RLF.
• All reproducible; trained model + demos committed to the repo.

## Slide 7
Result 1 — the energy-vs-QoS tradeoff
Heuristic sits near the efficient frontier; plain-reward PPO ties it byte-for-byte
4-seed averages. PPO reproduces the heuristic (a tie). Aggressive pruning saves more energy but costs reliability.

## Slide 8
Result 2 — an improved reward moved RL off the tie
Potential-based reward shaping -> a distinct, greener + more-reliable policy
Shaped-reward RL vs balanced heuristic (4-seed avg): +6 pts energy AND ~26% fewer dropped calls, ~9% less throughput.

## Slide 9
Why RL doesn't strictly dominate (the key insight)
• The heuristic is genuinely near-optimal here - it's hard to beat because it's already good.
• RL is sample-starved: the slow sim affords only ~640 trial-steps, and random on/off exploration
  – sleeps idle AND busy cells together -> can't isolate 'sleeping THIS idle cell was the good move'.
• The 43% 'idle-but-powered' waste is real in hindsight, but NOT free to reclaim: sleeping a
  – momentarily-idle cell that's needed next causes a dropped call. The heuristic's caution is justified.
• So it's a favourable TRADEOFF (greener + more reliable, slightly less throughput), not a clean sweep.

## Slide 10
Operational value — a tunable energy/QoS frontier
One dial lets an operator choose the operating point; the heuristic is a single fixed point
Pruning 'grace' dial: from the heuristic's point up to ~57% energy saved, trading throughput as you go.

## Slide 11
What the controller does over time
Cells sleep through the lulls and wake for the bursts
Power over time, # gNBs on, and which cell sleeps when. Idle cells sleep; busy cells stay on.

## Slide 12
Bottom line & recommended next step
• Delivered: a realistic bursty twin, a working imitation+RL pipeline (BC 100% match, stable PPO),
  – a rigorous quantification of the energy-vs-QoS tradeoff, and a tunable energy-saving controller.
• RL result: with reward shaping, RL learns a greener + more-reliable operating point than the heuristic
  – (better on energy and dropped-calls; slightly lower throughput) - a favourable, honest tradeoff.
• It does not STRICTLY beat a strong heuristic on all three axes - and we explain precisely why.
• Next step for a strict win: a spatial-HOTSPOT scenario (some cells persistently idle), where a smart
  – controller can sleep truly-unused cells for free - more realistic and genuinely winnable.

## Slide 13
Reproducibility & deliverables
• Two git repos: ns-3-mmwave-oran (the twin) + ns-o-ran-gym (gym / RL / analysis).
• Committed: trained model + demos + obs-stats; all scripts; figures computed live from run folders.
• Docs (self-contained): OVERVIEW.md (how it all works), RESULTS.md (findings & numbers),
  – REPRODUCE.md (build & run from scratch), CONTEXT.md (full-journey primer).
• Figures: energy-vs-QoS tradeoff, per-metric comparison, pruning frontier, controller-over-time.